## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
DESIGN AND SIMULATION OF A DIGITAL DOOR LOCK SYSTEM USING LOGIC GATES
A simple password-matching circuit
Team Members & Roll Numbers: K.Rithwik (2620040124)
G.Veerendranath Reddy (2620030373)
Deepak surya (2620090129)
Likith Chandra (2620040104)
Guide: Dr. Venkanna Isampalli
Department of Freshman Engineering | Academic Year 2026–27
01

## Slide 2
Introduction
Turning a correct digital code into an unlock signal
02
The idea
A digital door lock checks a binary password entered by the user.
Logic-gate approach
NOT and AND gates compare the entered bits with a preset code.
Expected result
Correct code → UNLOCK indicator ON
Incorrect code → LOCK indicator ON
This is an educational logic-circuit prototype, not a certified security lock.

## Slide 3
Objectives
Project goals
03
1
Design a basic digital door lock using logic gates.
2
Represent the password as a 4-bit binary code.
3
Build a Boolean expression that detects the correct code.
4
Test the circuit for correct and incorrect inputs.
5
Connect the project to digital design concepts in the course handout.

## Slide 4
COURSE OUTCOMES (COs)
Mapped to the six official outcomes in the course handout
CO1
Understand the basic organization of a computer system and represent digital information using binary number systems and logic gates as the foundation of digital computing.
CO2
Design and simulate combinational logic and build a simple Arithmetic Logic Unit (ALU) — the part of the processor that computes.
CO3
Design, analyze, and integrate sequential logic circuits including flip-flops, registers, shift registers, counters, program counter, and finite state machines for synchronous digital systems and RISC-V processor applications.
CO4
Design and implement the register file and memory subsystem of a processor, and explain the role of memory hierarchy in computer systems.
CO5
Analyze the execution of RISC-V instructions, develop simple RISC-V assembly programs, and integrate the data path and control unit to implement a functional single-cycle processor.
CO6
Enhance a single-cycle RISC-V processor by designing and implementing architectural extensions and peripheral interfaces using Project-Based Learning.
Project focus: CO1 (digital foundations) and CO2 (combinational logic design). CO3–CO6 are included as the full course outcomes.

## Slide 5
Components Required
Suggested parts for a simple demonstrator
05
Logic components
• 5 V DC supply
• NOT gate (e.g., 7404)
• AND gates (e.g., 7408)
• 4 input switches for A, B, C, D
• LEDs for LOCK and UNLOCK
• Current-limiting resistors
Build and test tools
• Breadboard and jumper wires
• Logic simulator: Logisim Evolution or Digital
• Optional: transistor/driver stage for a physical lock actuator
• Do not connect a door strike directly to logic IC outputs

## Slide 7
Circuit Working
Password match operation
07
1
The user enters four binary bits using switches A, B, C and D.
2
The preset password for this design is 1010.
3
NOT gates produce B̅ and D̅, needed because those password bits are 0.
4
An AND gate combines A, B̅, C and D̅ to detect the exact code.
5
When the expression is 1, UNLOCK turns ON; otherwise, LOCK remains ON.

## Slide 8
Truth Table
Preset code = 1010
08
1 = ON / HIGH | 0 = OFF / LOW
A | B | C | D | UNLOCK | LOCK
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 1

## Slide 9
Logic Design
Boolean expression for the preset code 1010
09
Required match
A = 1, B = 0, C = 1, D = 0
Boolean expression
UNLOCK = A · B̅ · C · D̅
Complemented bits
B̅ = NOT B and D̅ = NOT D
Lock indicator
LOCK = NOT(UNLOCK)
The AND output becomes HIGH only when all four required conditions are true.

## Slide 10
Advantages
Why this design is useful
11
1
Simple and inexpensive logic-circuit demonstration.
2
No software programming is required for the basic circuit.
3
Clearly demonstrates binary inputs, Boolean expressions and gates.
4
Easy to simulate and test using different code combinations.
5
Can be expanded into a larger digital access-control project.

## Slide 11
Limitations
Important design boundaries
12
1
A 4-bit code has only 16 possible combinations and is not secure for real use.
2
The basic circuit does not store failed attempts or limit repeated guesses.
3
Power loss and switch glitches may affect a physical prototype.
4
Logic-gate outputs cannot directly drive a high-current door lock actuator.
5
A practical product needs secure code storage, enclosure, and safety testing.

## Slide 12
Applications & Future Scope
Possible extensions beyond the basic model
13
Applications
• Digital logic laboratory demonstration
• Basic access-control prototype
• Learning project for Boolean logic
• Entry-level embedded hardware concept
Future improvements
• Increase password length
• Add a keypad interface
• Add a flip-flop/latch for state holding
• Add attempt counter and alarm
• Use a protected driver circuit for an actuator
Advanced features would introduce sequential logic (Module 3) and additional control design.

## Slide 13
Conclusion
A small practical example of digital design
14
What was designed
A logic circuit that recognizes the preset binary password 1010.
What it demonstrates
NOT and AND gates, Boolean expressions, truth tables, and combinational circuit testing.
The project connects Module 1 digital foundations with Module 2 combinational logic design.

## Slide 14
Project Files / GitHub
Add your repository URL after uploading your work
15
Repository Link
https://github.com/Rithwik-Builds/DDCA-Presentation
Suggested contents
PPT, circuit diagram, simulation file, truth table, project report.
README should include
Project aim, logic expression, how to simulate, test cases, team contributions.

## Slide 15
THANK YOU
Questions & Discussion
DIGITAL DOOR LOCK SYSTEM USING LOGIC GATES